## Slide 1: Fusion 360 Pill Box Walkthrough
1. Open Fusion 360 and save your design:
Ultimaker Core Lessons — STEAM set produced by Lizabeth Arum is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License.

## Slide 2
2. Name your design:
Ultimaker Core Lessons: STEAM — Lesson 2: Fusion 360 Pill Box Walkthrough — Page 2

## Slide 3
3. Create a sketch:
Ultimaker Core Lessons: STEAM — Lesson 2: Fusion 360 Pill Box Walkthrough — Page 3

## Slide 4
4. Select the XY plane to work on:
Ultimaker Core Lessons: STEAM — Lesson 2: Fusion 360 Pill Box Walkthrough — Page 4

## Slide 5
5. Create a circle with a diameter of 30:
Ultimaker Core Lessons: STEAM — Lesson 2: Fusion 360 Pill Box Walkthrough — Page 5

## Slide 6
6. The offset command can create concentric circles, parallel lines, and parallel curves. You can offset an object at a specified distance. Create an offset for the wall thickness of 1.2:
Ultimaker Core Lessons: STEAM — Lesson 2: Fusion 360 Pill Box Walkthrough — Page 6

## Slide 7
7. Stop the sketch. Press E to extrude. Extrude the bottom (interior circle) 1.2 mm. When you extrude your sketch, your sketch will turn off. In the Browser toggle the sketch’s visibility. Extrude the walls of the cylinder 30mm. Join these two extrusions to create a single object:
Ultimaker Core Lessons: STEAM — Lesson 2: Fusion 360 Pill Box Walkthrough — Page 7

## Slide 8
8. Select Create: Thread:
Ultimaker Core Lessons: STEAM — Lesson 2: Fusion 360 Pill Box Walkthrough — Page 8

## Slide 9
9. Set the parameters of the threads:
Select modeled.
Deselect Full Length.
Set Length to 5mm.
Select ISO metric profile.
Set the size to 30mm.
Set the class to M30x1.5.
Enable remember size.
Ultimaker Core Lessons: STEAM — Lesson 2: Fusion 360 Pill Box Walkthrough — Page 9

## Slide 10
10. Create a construction plane at the top of the cylinder. Select Construct: Offset Plane, then click on top of cylinder. Turn off the visibility of the cylinder:

## Slide 11
11. Create a new sketch and select the offset plane to sketch on. Select project or type P:

## Slide 12
12. Click on both circles:

## Slide 13
13. Stop the sketch:

## Slide 14
14. Extrude both circles up at least 3mm:

## Slide 15
15. Turn the last sketch on:

## Slide 16
16. Extrude the inner circle down 5mm. Select Join for the operation:

## Slide 17
17. Select Create: Thread:

## Slide 18
18. Apply the threads:

## Slide 19
19. Select the edges of the cap and apply a fillet:

## Slide 20
20. Apply a fillet to the top of the container and a chamfer to the bottom:
Ultimaker Core Lessons: STEAM — Lesson 2: Fusion 360 Pill Box Walkthrough — Page 20

## Slide 21
Rename bodies (Bottom and Top, Cylinder and Cap, or something similar).
Save your model.
Export your models. There are two ways to export your model as two separate parts:
  Export your model by Ctrl clicking on the Bottom and the Top in the Bodies menu in the Browser.
  Click Make: 3D Print from the Toolbar and select the Bottom. Save and then repeat for the Top.
Print!
Ultimaker Core Lessons: STEAM — Lesson 2: Fusion 360 Pill Box Walkthrough — Page 21