## Slide 1: Tinkercad Pill Box Walkthrough
1. Open a webGL-enabled browser like Chrome or Safari. Navigate to https://www.tinkercad.com. Sign up or sign in:
Ultimaker Core Lessons — STEAM set produced by Lizabeth Arum is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License.

## Slide 2
2. Create a new design:
Ultimaker Core Lessons: STEAM — Lesson 2: Tinkercad Pill Box Walkthrough — Page 2

## Slide 3
3. The first part to design is the cap. Make a cylinder 30 x 30 x 20.
4. To add shapes, letters or numbers, drag an instance from the palette on the right over to the workplane. Drag a cylinder from the left on to the workplane:
Ultimaker Core Lessons: STEAM — Lesson 2: Tinkercad Pill Box Walkthrough — Page 3

## Slide 4
5. For a smoother cylinder, increase the number of sides and segments:
Ultimaker Core Lessons: STEAM — Lesson 2: Tinkercad Pill Box Walkthrough — Page 4

## Slide 5
6. The first way to change the dimensions is by dragging the nodes to the desired values. The second way is to press R and place ruler on the workplane. Then enter the dimensions into the appropriate fields:
Ultimaker Core Lessons: STEAM — Lesson 2: Tinkercad Pill Box Walkthrough — Page 5

## Slide 6
7. Drag an instance of a Hole Cylinder onto the workplane:
Ultimaker Core Lessons: STEAM — Lesson 2: Tinkercad Pill Box Walkthrough — Page 6

## Slide 7
8. You want a wall thickness of 1.5mm, so set the Width to 27, Length to 27 and leave the Height at 20:
Ultimaker Core Lessons: STEAM — Lesson 2: Tinkercad Pill Box Walkthrough — Page 7

## Slide 8
9. Click and drag the black cone of the Hole so that the Cylinder raises 2mm off the workplane, or change the value in the box:
Ultimaker Core Lessons: STEAM — Lesson 2: Tinkercad Pill Box Walkthrough — Page 8

## Slide 9
Select both cylinders and select Align.
Click on the center nodes to align the objects:
Ultimaker Core Lessons: STEAM — Lesson 2: Tinkercad Pill Box Walkthrough — Page 9

## Slide 10
12. Make sure both cylinders are selected and click on Group:

## Slide 11
13. Drag another instance of a Cylinder onto the workplane. Set the Width to 30, Length to 30 and Height to 2mm:

## Slide 12
14. Drag another instance of a Cylinder and set the Width to 26, to Length 26 and Height to:

## Slide 13
15. Drag another instance of a Hole Cylinder onto the workplane. Set the Width to 23, Length to 23 and Height to 18:

## Slide 14
16. You need to create a rim for friction. Drag another instance of a Cylinder out and set the Width to 27, Length to 27, and Height to 2mm:

## Slide 15
17. Move the last cylinder you added 14mm off the workplane:

## Slide 16
18. Select the last three cylinders by Shift left clicking each of them and then align them together:

## Slide 17
19. Drag an instance of a Box on to the workplane and set the width to 28 mm, Length to 2 mm, and Height to 14 mm:

## Slide 18
20. Duplicate in place by selecting the box and pressing CTRL/Command+D. Then rotate the duplicated box 90°. Hold Shift when rotating:

## Slide 19
21. Convert to Hole:

## Slide 20
22. Raise the cross 2mm up from the workplane:

## Slide 21
23. Align the cross with the last group of cylinders:

## Slide 22
24. Group the aligned objects:

## Slide 23
25. Raise the grouped cylinders up 2mm and align with the cap (the cylinder that is 2mm high):

## Slide 24
26. Group the cylinders and cap.
27. Rename the model:

## Slide 25
1. Export the the two parts together or separately.
2. Print.