## Slide 1: Tinkercad Flashlight Walkthrough
1. Open a webgl-enabled browser like Chrome or Safari. Navigate to https://www.tinkercad.com. Sign up or sign in:
Ultimaker Core Lessons — STEAM set produced by Lizabeth Arum is licensed under a Creative Commons Attribution-ShareAlike 4.0 International License.

## Slide 2
2. Create a new design:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 2

## Slide 3
Things to keep in mind :
  The diameter of the PVC tube is 21.45 mm.
  To create a tight fit, make your hole smooth and set the diameter to 21.70 mm.
  The Tinkercad coin cell holder has a diameter of 32.25 mm. You don’t want quite as tight a fit (you could break the print if you apply to much force), so make the hole smooth and give it a diameter of 32.60mm
  Make sure you smooth every shape.
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 3

## Slide 4
4. If you are pre printing the Tinkercad coin cell holders, skip this step, otherwise drag an instance of the Glow onto the workplane. Then reset the menu to Basic Shapes:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 4

## Slide 5
Create the base by creating 3 cylinders.
Make the first one: 35.45 mm x 35.45 mm x 27 mm. Make the cylinder smooth:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 5

## Slide 6
7. You want a wall thickness of 1.2mm so make the first hole 32.6 mm x 32.6 mm x 26 mm. Make the hole smooth:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 6

## Slide 7
8. Drag an instance of a Cylinder onto the workplane and set it to 35.45 mm x 35.45 mm x 3 mm. Make the cylinder smooth. Raise this cylinder 24 mm up of the workplane:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 7

## Slide 8
9. Drag an instance of a Cylinder onto the workplane and set it to 24.1 mm x 24.1 mm x 4 mm. Make it smooth. Move it up 27 mm:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 8

## Slide 9
10. Drag an instance of a Cylinder Hole and make it 21.7 mm x 21.7 mm x 7 mm, make it smooth, and raise it up 24 mm:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 9

## Slide 10
11. Align all the cylinders:

## Slide 11
12. Group all the cylinders:

## Slide 12
Create a top piece.
Drag an instance of the Cylinder to the workplane. Set the dimensions to 40.1 mm 40.1 mm x 26 mm cylinder. Make it smooth. Then drag an instance of the Cylinder Hole to the workplane. Set the dimensions to 37.7 mm x 37.7 mm x 26 mm. Make it smooth:

## Slide 13
15. Drag an instance of the Cone to the workplane. Set the dimensions to 40.10 mm 40.10 mm x 40 mm cone: Make it smooth by increasing sides. Raise it up 26 mm:

## Slide 14
16. Make a copy of the cone and set the dimensions to 37.7 mm x 37.7 mm x 38.9 mm. Convert it to a hole:

## Slide 15
17. Drag an instance of the Cylinder to the workplane. Set the dimension to 24.1 mm x 24.1 mm x 4 mm. Make it smooth and raise it up 42mm:

## Slide 16
18. Drag an instance of the Cylinder Hole to the workplane. Set the dimension to 21.70 mm x
21.7 mm x 4mm. Make it smooth and raise it up 42 mm:

## Slide 17
19. Align the objects:

## Slide 18
20. Drag an instance of a Cylinder Hole on to the workplane. Make it 30 mm x 30 mm x 30 mm and raise it 46 mm. Align it so that it would delete the top of the cone:

## Slide 19
21. Group these objects together:

## Slide 20
Create image discs to create shadow images on the wall.
Drag an instance of a Cylinder on to the workplane and set the dimensions to 40.1 mm x
40.1 mm x 1 mm. Make it smooth:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 20

## Slide 21
24. Find an SVG online or create your own. Save on your computer.
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 21

## Slide 22
25. In Tinkercad click on the import button and set the width to 20 mm.
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 22

## Slide 23
26. Use your object as hole or a positive and create a few discs that are no higher than 1 mm.
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 23

## Slide 24
27. Now you need to create a cap to hold the disc in place. Drag an instance of a Cylinder on to the workplane and set the dimensions to 44.10 mm x 44.10 mm x 2 mm cylinder. Make it smooth:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 24

## Slide 25
28. Drag an instance of a Cylinder Hole on to the workplane and set the dimensions to 34 mm x 34 mm x 2 mm. Make it smooth:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 25

## Slide 26
29. Drag an instance of a Cylinder on to the workplane and set the dimensions to 44.10 mm x
44.10 mm x 5 mm. Make it smooth and raise it up 2mm:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 26

## Slide 27
30. Drag an instance of a Cylinder Hole on to the workplane and set the dimensions to 40.55 mm x 40.55 mm x 5 mm. Make it smooth and raise it up 2mm:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 27

## Slide 28
31. Align cylinders:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 28

## Slide 29
32. Group the cylinders:
Ultimaker Core Lessons: STEAM — Lesson 3: Tinkercad Flashlight Walkthrough — Page 29

## Slide 30
33. Rename the model:

## Slide 31
Export the parts separately.
Print.
Connect the parts together.
Play.
Brainstorm:
What would make this design better?
Does it need a switch?
Should there be an easier way to switch the discs?
39. Iterate.