## Slide 1: Espinha de peixe (Diagrama Ishikawa)
Declaração do Problema
Homem/Mulher
Máquina
Materiais
Método
Causas
Efeitos
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 2: Tópicos Avançados)
2.Mapeie o processo
3.Estabeleça um fluxo
4. Implement Pull
5. Trabalhe em busca da perfeição
1.Especifique o valor
Definição de valor pela perspectiva do cliente
A completa eliminação do desperdício em todas as atividades que não agregam valor ao cliente
Mapeie todas as fases as que geram valor e as que não geram
O movimento contínuo dos serviços e informações através do processo
Nada é feito no processo de cima para baixo até que o cliente dê sinais da necessidade
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 3: Espinha de peixe (Diagrama Ishikawa)
CAUSAS E EFEITOS 6M
Método
Matéria-Prima
Mão-de-obra
Máquinas
Medição
Meio Ambiente
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 4: TOPICOS AVANÇADOS
Estratégia é o padrão de objetivos, fins ou metas e principais políticas e planos para atingir esses objetivos, estabelecidos de forma a definir qual o negócio em que a empresa está e o tipo de empresa que é ou vai ser.
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 5: TOPICOS AVANÇADOS
Estratégia competitiva são ações ofensivas ou defensivas para criar uma posição defensável numa indústria, para enfrentar com sucesso as forças competitivas e assim obter um retorno maior sobre o investimento.
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 6: TOPICOS AVANÇADOS
OBJETIVOS DA ESTRATÉGIA DE NEGÓCIO
Proporcionar visão estruturada do Processo Estratégico;
Capacitar na utilização das principais ferramentas de análise;
Desenvolver a capacidade decisória estratégica dos participantes.
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 7: TOPICOS AVANÇADOS
Estratégia. Para que serve?
Identificar e capturar oportunidades;
Identificar e neutralizar ameaças;
Sustentar ou expandir posições conquistadas;
Equacionar crises.
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 8: Oceano azul
Em busca de um crescimento sustentável e lucrativo, de olho em fatias generosas do mercado e trabalhando para tornar seus produtos — ou serviços — diferenciados em meio à concorrência, muitas empresas entram numa roda-viva de competição bruta, pesada. O resultado dessa “batalha” é um “oceano vermelho”, nascido da luta sangrenta entre rivais por um potencial de lucros muitas vezes decrescente. Esse é o problema, segundo W. Chan Kim e Renée Mauborgne, autores de A Estratégia do Oceano Azul. Eles ensinam: “Não concorra com os rivais — torne-os irrelevantes”.
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 9: TOPICOS AVANÇADOS
INOVAÇÃO
Objetivamos ser pioneiros nas nossas inovações
Buscamos inovar em tudo que fazemos, em todas as áreas, processos e momentos
Ousamos baseados nos desejos do consumidor
Buscamos a liderança de mercado construindo marcas fortes
Questionamos as situações estabelecidas
Temos coragem para tomar risco e buscamos aprender com os erros cometidos.
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 10: TOPICOS AVANÇADOS
De empresa e setor para iniciativa estratégica
Como uma empresa será capaz de transpor os limites do oceano vermelho da competição sangrenta?
Como poderá criar oceanos azuis?
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 11: TOPICOS AVANÇADOS
Por que Aprender a Argumentar?
Gerenciando Informação
Gerenciando Relação
Argumentar, Convencer e Persuadir
Um Pouco de História
Tarefas da Retórica Clássica
Senso Comum, Paradoxo e Maravilhamento
Condições da Argumentação
O Auditório
Auditório Universal e Auditório Particular
Convencendo as Pessoas
As Técnicas Argumentativas
Argumentos Quase Lógicos
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 12: TOPICOS AVANÇADOS
Argumentos Fundamentados na Estrutura do Real
Dando Visibilidade aos Argumentos – Os Recursos de Presença
Persuadindo as Pessoas
Emoções e Valores
As Hierarquias de Valores
Alterando a Hierarquia de Valores - Os Lugares da Argumentação
Lugar de Quantidade
Lugar de Qualidade
Lugar de Ordem
Lugar de Essência
Lugar de Pessoa
Lugar do Existente
Afinal de Contas, o Que É Argumentar?
Aprendendo a ”Desenhar” e a ”Pintar” com as Palavras
Figuras Retóricas
Figuras de Som
Figuras de Palavra
Metonímia
Metáfora
Figuras de Construção
Pleonasmo
Hipálage
Anáfora
Epístrofe
Concatenação
Figuras de Pensamento
Antítese
Paradoxo
Alusão
Conclusão
Palavras Finais
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 13: TOPICOS AVANÇADOS
Lugar do Existente
Afinal de Contas, o Que É Argumentar?
Aprendendo a ”Desenhar” e a ”Pintar” com as Palavras
Figuras Retóricas
Figuras de Som
Figuras de Palavra
Metonímia
Metáfora
Figuras de Construção
Pleonasmo
Hipálage
Anáfora
Epístrofe
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.

## Slide 14: TOPICOS AVANÇADOS
Concatenação
Figuras de Pensamento
Antítese
Paradoxo
Alusão
Conclusão
Palavras Finais
Notes: 4 M’s - Man, Materials, Method, Machine
Various names: Ishikawa diagram, Cause-and-Effect diagram, Fishbone diagram, Root Cause Analysis
Definition: A graphic tool used to explore and display opinion about sources of variation in a process. (Also called a Cause-and-Effect or Fishbone Diagram.)
Purpose: To arrive at a few key sources that contribute most significantly to the problem being examined. These sources are then targeted for improvement. The diagram also illustrates the relationships among the wide variety of possible contributors to the effect.
The basic concept in the Cause-and-Effect diagram is that the name of a basic problem of interest is entered at the right of the diagram at the end of the main "bone". The main possible causes of the problem (the effect) are drawn as bones off of the main backbone. The "Four-M" categories are typically used as a starting point: "Materials", "Machines", "Manpower", and "Methods". Different names can be chosen to suit the problem at hand, or these general categories can be revised. The key is to have three to six main categories that encompass all possible influences. Brainstorming is typically done to add possible causes to the main "bones" and more specific causes to the "bones" on the main "bones". This subdivision into ever increasing specificity continues as long as the problem areas can be further subdivided. The practical maximum depth of this tree is usually about four or five levels. When the fishbone is complete, one has a rather complete picture of all the possibilities about what could be the root cause for the designated problem.
The Cause-and-Effect diagram can be used by individuals or teams; probably most effectively by a group. A typical utilization is the drawing of a diagram on a blackboard by a team leader who first presents the main problem and asks for assistance from the group to determine the main causes which are subsequently drawn on the board as the main bones of the diagram. The team assists by making suggestions and, eventually, the entire cause and effect diagram is filled out. Once the entire fishbone is complete, team discussion takes place to decide what are the most likely root causes of the problem. These causes are circled to indicate items that should be acted upon, and the use of the tool is complete.
How to Construct:
Place the main problem under investigation in a box on the right.
Have the team generate and clarify all the potential sources of variation.
Use an affinity diagram to sort the process variables into naturally related groups. The labels of these groups are the names for the major bones on the Ishikawa diagram.
Place the process variables on the appropriate bones of the Ishikawa diagram.
Combine each bone in turn, insuring that the process variables are specific, measurable, and controllable. If they are not, branch or “explode” the process variables until the ends of the branches are specific, measurable, and controllable.
Tips:
Take care to identify causes rather than symptoms.
Post diagrams to stimulate thinking and get input from other staff.
Self-adhesive notes can be used to construct Ishikawa diagrams. Sources of variation can be rearranged to reflect appropriate categories with minimal rework.
Insure that the ideas placed on the Ishikawa diagram are process variables, not special caused, other problems, tampering, etc.
Review the quick fixes and rephrase them, if possible, so that they are process variables.