## Slide 1: Leverage Your Renewable Energy Impact Through Emerging Avoided Emissions PPA Strategies
AASHE 2018

## Slide 2: Workshop Facilitators
Boston University
  Dennis Carlberg, Associate VP for University Sustainability carlberg@bu.edu
  Casey Kelly, sustainability@BU Intern caseyk@bu.edu
Carnegie Mellon University, Center for Climate and Energy Decision Making
  Inês Azevedo, Co-Director iazevedo@cmu.edu
Edison Energy (formerly Altenex)
  Christen Blum, christen.blum@edisonenergy.com Advisory Renewables Managing Director
WattTime
  Gavin McCormack, Co-Founder and Executive Director gavin@watttime.org
Notes: Y

## Slide 3: Terms
Additionality
Purpose of RECs
Accounting with RECs
Power Purchase Agreements
Avoided Emissions and their Calculations
Marginal Emissions and their Calculations
eGrid Emissions and their Calculations
Scope 2 Accounting
Inventory Based Accounting
Impact Based Accounting
Notes: ??

## Slide 4: How does renewable energy help the environment?

## Slide 5: How does renewable energy help the environment?
X

## Slide 6: But which fossil plants will your renewables replace?

## Slide 7: But which fossil plants will your renewables replace?

## Slide 8: But which fossil plants will your renewables replace?

## Slide 9: CMU’s research makes it possible to know
Projects in
California displace
mostly natural gas
Projects in
Georgia displace
mostly coal

## Slide 10: BU decided to multiply their impact
Renewables in Boston
reduce emissions
a little
Renewables in some regions reduce
emissions a lot

## Slide 11: Edison handled economics and site selection
Solar in CA
can save
~900 kg/kW
Wind in Texas
can, too…
but at a better price

## Slide 12: WattTime verified & is raising awareness
BU’s strategy
increased
emissions savings

## Slide 13: Themes
Inventory-based Accounting
Average emissions
All MWh count equally
Priority is ensuring all emissions are “owned” by someone
Cumulative, predictable
Market-based
Impact-based Accounting
Marginal emissions
Counts MWh based on actual emissions
Priority is accurately measuring actual effects of actions
Physics-based
Project Impact
Emissions
Environmental
Financial
Process
Goal setting
Procurement
eGRID and marginal emissions analysis
Marginal emissions data collection
1
3
2
4
Notes: Gavin

## Slide 14: Boston University Project Drivers
Climate Action Plan goal
Carbon Impact
Additionality
Credible, Verifiable, Project RECs
Postive Economics
Benefit Student Education and Faculty Research

## Slide 15: Process
Project Generation Profile
(Edison)
Marginal Emissions Profile
(CMU)
127
68 Wind & 59 Solar Projects
Data Analysis (BU)
7 Wind
4 Solar
Projects
Economic & eGrid Screen
2 Wind
1 Solar
Projects
South Dakota Wind Project
Economics & Risk Screen
Criteria Due Diligence
Team Interviews
WattTime Marginal Emissions Validation
Marginal Emissions Screen
LOI / Term Sheet
to
REPA Contract

## Slide 16: Align Generation with Marginal Emissions
Chart: 
Wind 7 Emissions | 610.8608 | 678.4778 | 705.8301 | 731.9615 | 706.1372 | 650.9384 | 631.8284 | 665.8768 | 627.2536 | 629.634 | 607.7317 | 602.4352 | 621.1141 | 618.4103 | 617.7859 | 636.8573 | 640.8359 | 624.9624 | 619.3273 | 619.9609 | 618.3229 | 620.7412 | 579.3763 | 588.0341
MW Generation
Marginal Emissions (kg/MWh)
Notes: Casey

## Slide 17: Net Zero Direct Emissions by 2040
Electricity
Natural Gas
Steam
Oil
2050 CarbonFree Boston
2040
25% reduction by 2016
Carbon Free Boston
BU Institute for Sustainable Energy
Leadership
Notes: Dennis

## Slide 18: Net Zero Direct Emissions by 2040
Electricity
Natural Gas
Steam
Oil
Net Zero by 2040
Assumptions
Campus Growth
0.75% / year
Notes: Dennis

## Slide 19: Net Zero Direct Emissions by 2040
Electricity
Natural Gas
Steam
Oil
Efficiency
Net Zero by 2040
Strategies
Energy Efficiency
31% by 2032
New Buildings
EUI 90 kBtu/sf
Notes: Dennis

## Slide 20: Net Zero Direct Emissions by 2040
Electricity
Natural Gas
Steam
Oil
Efficiency
Net Zero by 2040
Assumptions
Greener Grid
1.25% / year
Grid
Notes: Dennis

## Slide 21: Net Zero Direct Emissions by 2040
Electricity
Natural Gas
Steam
Oil
Efficiency
Net Zero by 2040
Strategies
Renewable Energy
100% starting in 2019
Grid
Renewables
Notes: Dennis

## Slide 22: Net Zero Direct Emissions by 2040
Electricity
Natural Gas
Steam
Oil
Efficiency
Net Zero by 2040
Strategies
Electrify Heating
End of useful life
Source with Renewables
100%
Grid
Renewables
Electrification with Renewables
Notes: Dennis

## Slide 23: Net Zero Direct Emissions by 2040
Electricity
Natural Gas
Steam
Oil
Net Zero by 2040
Strategies
Offsets
Shortfall to reach 100% starting in 2040
Grid
Renewables
Electrification with Renewables
Offsets
Efficiency
Notes: Dennis

## Slide 24: Leadership
Notes: Dennis

## Slide 25: How can we quantify the emissions (GHG and air pollutants) and the respective damages that are avoided as we pursue different interventions in the U.S. electric grid?
Notes: Ines

## Slide 26: Are we helping the environment more by increasing solar in California or in Pennsylvania?
???

## Slide 27: Are we helping the environment more if we choose a battery electric car or an hybrid?

## Slide 28: In which states can we have the largest environmental and health benefits from more stringent building codes?

## Slide 29: Where can we have the largest environmental and health benefits from increasing wind energy?

## Slide 30: Are we helping the environment by increasing storage in our electricity grid?

## Slide 31: The US grid is diverse in its carbon intensity
Attribution: figure produced by Nathaniel Horner using data from CEMS and EIA.
metric tCO2/MWh
State level CO2 emissions factors for total electricity generation 2015

## Slide 32: The US grid is diverse in its carbon intensity
CO2 marginal emissions factors by U.S. power grid, Sept 12 2018

## Slide 33: Damages from criteria air pollutants vary tremendously across the country
Source: Based on AP2 model from Prof. N. Muller
$1000/ton SO2
$15,000/ton SO2

## Slide 34
Power sector interventions (solar installation, demand response, adding electric vehicles, etc.) change emissions at the margin.
Fossil fuel generation produces emissions that contribute to climate change and harm health/environment.
Chart: Total Demand (GW)
| 1038.978894389953 | 2038.978894389953
Hydro | 10 | 10
 | 28.0935 | 28.4393 | 29.061 | 29.1108 | 29.425 | 32.7373 | 33.0631 | 37.6957 | 39.5817 | 39.8514 | 42.6703 | 44.0822
NG | 17.7546 | 19.1588
NG | 44.7675
NG | 48.835 | 54.7029 | 77 | 80 | 100 | 120 | 150 | 175 | 190 | 200
Nuc | 15 | 16 | 16.9557
Figures adapted from Azevedo. This is a schematic only; it does not represent a real system.
Chart: Total Demand (GW)
| 1038.978894389953 | 2038.978894389953
Hydro | 0 | 0
 | 869.733 | 850 | 832.2944 | 831.3533 | 826.9837 | 879.8831 | 875.3042 | 842.2096 | 811.6445 | 848.2829 | 804.2178 | 882.6515
NG | 431.2723 | 474.6255
NG | 466.3609
NG | 496.1822 | 495.7389 | 465.3717 | 459.9297 | 431.9459 | 432.6113 | 422.3358 | 491.9555 | 461.398 | 412.8333
Nuc | 0 | 0
Fossil fuel generation produces emissions that contribute to climate change and harm health/environment.
Notes: Electricity provides huge benefits to society. 2017: 2/3 of U.S. electricity from fossil fuels
More specifically, at any given time, electricity generators bid some cost at which they're willing to provide electricity (on the y-axis), and we use these generators from least to greatest cost (cumulative generation on x-axis).
Each generator has some emissions intensity (or "emissions factor") associated with it (here shown for CO2) (Make sure to refer to the green arrows.)
The total emissions produced corresponds to the integral under this emissions factor curve.
In this work, we call this power system interventions

## Slide 35
Power sector interventions (solar installation, demand response, adding electric vehicles, etc.) change emissions at the margin.
Fossil fuel generation produces emissions that contribute to climate change and harm health/environment.
Chart: Total Demand (GW)
| 1038.978894389953 | 2038.978894389953
Hydro | 10 | 10
 | 28.0935 | 28.4393 | 29.061 | 29.1108 | 29.425 | 32.7373 | 33.0631 | 37.6957 | 39.5817 | 39.8514 | 42.6703 | 44.0822
NG | 17.7546 | 19.1588
NG | 44.7675
NG | 48.835 | 54.7029 | 77 | 80 | 100 | 120 | 150 | 175 | 190 | 200
Nuc | 15 | 16 | 16.9557
Figures adapted from Azevedo. This is a schematic only; it does not represent a real system.
Chart: Total Demand (GW)
| 1038.978894389953 | 2038.978894389953
Hydro | 0 | 0
 | 869.733 | 850 | 832.2944 | 831.3533 | 826.9837 | 879.8831 | 875.3042 | 842.2096 | 811.6445 | 848.2829 | 804.2178 | 882.6515
NG | 431.2723 | 474.6255
NG | 466.3609
NG | 496.1822 | 495.7389 | 465.3717 | 459.9297 | 431.9459 | 432.6113 | 422.3358 | 491.9555 | 461.398 | 412.8333
Nuc | 0 | 0
∆generation
∆emissions
Assumptions matter: e.g. annual average emissions factors mask marginal effects.
Captured by regressing hourly observed changes in emissions on hourly changes in (marginal) generation:
MEF (kg/MWh)
Notes: We don't know this curve (dispatch curve), and so the literature has looked at ways to estimate the emissions avoided by an intervention.
Different assumptions matter when evaluating interventions -- for instance, if instead of using marginal emissions factors (those associated with the natural gas plants we knocked out), we used average factors incorporating the dirty coal plants in the middle, we might overestimate the effectiveness of this intervention.
... and this could flip policy decisions

## Slide 36: Data
Hourly emissions and hourly generation for fossil fuel power plants larger than 25 MW (2006-17)
  Generation, CO2, SO2, NOx from EPA’s Continuous Emissions Monitoring System (CEMS) database
  PM2.5 from EPA’s National Emissions Inventory (NEI)
Coupling the emissions with the marginal damages of a ton of pollutant using air quality models (AP2 and EASIUR)
Notes: "The fuel types of marginal generators in every hour"

## Slide 37: Energy: Grid Mix
Generation Mix based on 2017 ISO Data, by MWh
Emissions Data based on eGrid 2014 v2 Data by NERC Region: SPP represents average of SPNO, SPSO, MROW, PJM represents average of SRVC, RFCW, RFCE, MISO represents average of RFCM, MROE, MROW, SRMW
SPP 2 to 3 > ISO-NE
1,482 lbs. CO2e/MWh
577 lbs. CO2e/MWh
1,148 lbs. CO2e/MWh
1,405 lbs. CO2e/MWh
1,029 lbs. CO2e/MWh
Notes: Inês > Dennis
Numbers being made during decision-making mode? > generation mix (2017) > eGRID (were mismatched to what we used) > these were the numbers
All the same scale [

## Slide 38: Energy: Criteria for Renewables
1
2
3
4
5
Impact: Greenhouse Gas Reduction
Additionality
Other Environmental Impacts
Education & Research
Project Economics
The projects we select should displace fossil fuel used for generating power on the economic margin for a large majority of operating conditions.
Chosen projects should generate new renewable power that would not otherwise be generated. Purchasing power through a 1-15 yr. enables developers to obtain financing to get projects built.
All projects have some environmental impact. We want to choose projects with lower construction and operational environmental impacts.
Projects will need to ensure they will benefit BU students and faculty by allowing access to the project sites and real time data and visualization.
Obtaining the most favorable project economics will help direct resources to other opportunities for emissions reductions.
Notes: Dennis

## Slide 39: Comparison of Renewable Energy Project Selection Criteria
Criteria | Weight | Solar 2 | Wind 7 | Wind 9 | Criteria Explanation | Notes
 |  | Weighted Rank |  |  |  | 
Impact New Build | Required |  |  |  | Project will generate new renewable power that would not otherwise have been generated | Project additionality is a prerequisite
Education & Research Opportunities | Required |  |  |  | Project will benefit students and faculty by allowing access to the project sites and real time data | Access to real time data and access to the project site(s) is a prerequisite
Green-e Certified RECs | Required |  |  |  | Third party certified project-based RECs | Project-based Green-e Certified RECs are necessary to validate the claims for the emissions reductions
Project Developer Financial Strength | Required |  |  |  | Long-term owner/operators have resources, experience, & financial strength to manage relationship over term | 
Bid Size Flexibility | Required |  |  |  | Ability to provide 200,000 MWh/yr or 100,000 MWh/yr capacity to allow flexibility on strategy as determined by BU | 
Weighted Rank
Notes: Dennis

## Slide 40: Comparison of Renewable Energy Project Selection Criteria
Criteria | Weight | Solar 2 | Wind 7 | Wind 9 | Criteria Explanation | Notes
 |  | Weighted Rank |  |  |  | 
Impact New Build | Required |  |  |  | Project will generate new renewable power that would not otherwise have been generated | Project additionality is a prerequisite
Education & Research Opportunities | Required |  |  |  | Project will benefit students and faculty by allowing access to the project sites and real time data | Access to real time data and access to the project site(s) is a prerequisite
Green-e Certified RECs | Required |  |  |  | Third party certified project-based RECs | Project-based Green-e Certified RECs are necessary to validate the claims for the emissions reductions
Project Developer Financial Strength | Required |  |  |  | Long-term owner/operators have resources, experience, & financial strength to manage relationship over term | 
Bid Size Flexibility | Required |  |  |  | Ability to provide 200,000 MWh/yr or 100,000 MWh/yr capacity to allow flexibility on strategy as determined by BU | 
Project Economics (strong NPV/MWh) | 30% | 3 | 1 | 2 | Financial strength based on risk-adjusted, projected cash flows, and impact on BU financial position and credit rating | The driver in a Contract for Differences is the margin modeled between the PPA price and the grid price/MWh. Favorable project economics are a prerequisite
Weighted Rank
Notes: Dennis

## Slide 41: Comparison of Renewable Energy Project Selection Criteria
Criteria | Weight | Solar 2 | Wind 7 | Wind 9 | Criteria Explanation | Notes
 |  | Weighted Rank |  |  |  | 
Impact New Build | Required |  |  |  | Project will generate new renewable power that would not otherwise have been generated | Project additionality is a prerequisite
Education & Research Opportunities | Required |  |  |  | Project will benefit students and faculty by allowing access to the project sites and real time data | Access to real time data and access to the project site(s) is a prerequisite
Green-e Certified RECs | Required |  |  |  | Third party certified project-based RECs | Project-based Green-e Certified RECs are necessary to validate the claims for the emissions reductions
Project Developer Financial Strength | Required |  |  |  | Long-term owner/operators have resources, experience, & financial strength to manage relationship over term | 
Bid Size Flexibility | Required |  |  |  | Ability to provide 200,000 MWh/yr or 100,000 MWh/yr capacity to allow flexibility on strategy as determined by BU | 
Project Economics (strong NPV/MWh) | 30% | 3 | 1 | 2 | Financial strength based on risk-adjusted, projected cash flows, and impact on BU financial position and credit rating | The driver in a Contract for Differences is the margin modeled between the PPA price and the grid price/MWh. Favorable project economics are a prerequisite
GHG Reduction (CO2e lb/MWh) | 30% | 3 | 1 | 2 | Projected likely marginal GHG savings per MWh over the term of the project; favor projects with highest overall GHG reduction with consideration for higher early reductions | Strong correlation between high grid carbon intensity at time of renewable energy production; the purpose of is to maximize the BU’s impact on GHG reduction
Weighted Rank
Notes: Dennis

## Slide 42: Comparison of Renewable Energy Project Selection Criteria
Criteria | Weight | Solar 2 | Wind 7 | Wind 9 | Criteria Explanation | Notes
 |  | Weighted Rank |  |  |  | 
Impact New Build | Required |  |  |  | Project will generate new renewable power that would not otherwise have been generated | Project additionality is a prerequisite
Education & Research Opportunities | Required |  |  |  | Project will benefit students and faculty by allowing access to the project sites and real time data | Access to real time data and access to the project site(s) is a prerequisite
Green-e Certified RECs | Required |  |  |  | Third party certified project-based RECs | Project-based Green-e Certified RECs are necessary to validate the claims for the emissions reductions
Project Developer Financial Strength | Required |  |  |  | Long-term owner/operators have resources, experience, & financial strength to manage relationship over term | 
Bid Size Flexibility | Required |  |  |  | Ability to provide 200,000 MWh/yr or 100,000 MWh/yr capacity to allow flexibility on strategy as determined by BU | 
Project Economics (strong NPV/MWh) | 30% | 3 | 1 | 2 | Financial strength based on risk-adjusted, projected cash flows, and impact on BU financial position and credit rating | The driver in a Contract for Differences is the margin modeled between the PPA price and the grid price/MWh. Favorable project economics are a prerequisite
GHG Reduction (CO2e lb/MWh) | 30% | 3 | 1 | 2 | Projected likely marginal GHG savings per MWh over the term of the project; favor projects with highest overall GHG reduction with consideration for higher early reductions | Strong correlation between high grid carbon intensity at time of renewable energy production; the purpose of is to maximize the BU’s impact on GHG reduction
Environmental& Health Co-benefits | 20% | 2 | 1 | 2 | Favor projects with lower construction and operational environmental and health impacts | 
Weighted Rank
Notes: Dennis

## Slide 43: Comparison of Renewable Energy Project Selection Criteria
Criteria | Weight | Solar 2 | Wind 7 | Wind 9 | Criteria Explanation | Notes
 |  | Weighted Rank |  |  |  | 
Impact New Build | Required |  |  |  | Project will generate new renewable power that would not otherwise have been generated | Project additionality is a prerequisite
Education & Research Opportunities | Required |  |  |  | Project will benefit students and faculty by allowing access to the project sites and real time data | Access to real time data and access to the project site(s) is a prerequisite
Green-e Certified RECs | Required |  |  |  | Third party certified project-based RECs | Project-based Green-e Certified RECs are necessary to validate the claims for the emissions reductions
Project Developer Financial Strength | Required |  |  |  | Long-term owner/operators have resources, experience, & financial strength to manage relationship over term | 
Bid Size Flexibility | Required |  |  |  | Ability to provide 200,000 MWh/yr or 100,000 MWh/yr capacity to allow flexibility on strategy as determined by BU | 
Project Economics (strong NPV/MWh) | 30% | 3 | 1 | 2 | Financial strength based on risk-adjusted, projected cash flows, and impact on BU financial position and credit rating | The driver in a Contract for Differences is the margin modeled between the PPA price and the grid price/MWh. Favorable project economics are a prerequisite
GHG Reduction (CO2e lb/MWh) | 30% | 3 | 1 | 2 | Projected likely marginal GHG savings per MWh over the term of the project; favor projects with highest overall GHG reduction with consideration for higher early reductions | Strong correlation between high grid carbon intensity at time of renewable energy production; the purpose of is to maximize the BU’s impact on GHG reduction
Environmental& Health Co-benefits | 20% | 2 | 1 | 2 | Favor projects with lower construction and operational environmental and health impacts | 
Integration with BU on-site procurement | 10% | 1 | 1 | 1 | Integrate PPA purchases and sales into BU's energy purchasing through hedges or other mechanisms | 
Weighted Rank
Notes: Dennis

## Slide 44: Comparison of Renewable Energy Project Selection Criteria
2.5 | 1.1 | 1.8
Criteria | Weight | Solar 2 | Wind 7 | Wind 9 | Criteria Explanation | Notes
 |  | Weighted Rank |  |  |  | 
Impact New Build | Required |  |  |  | Project will generate new renewable power that would not otherwise have been generated | Project additionality is a prerequisite
Education & Research Opportunities | Required |  |  |  | Project will benefit students and faculty by allowing access to the project sites and real time data | Access to real time data and access to the project site(s) is a prerequisite
Green-e Certified RECs | Required |  |  |  | Third party certified project-based RECs | Project-based Green-e Certified RECs are necessary to validate the claims for the emissions reductions
Project Developer Financial Strength | Required |  |  |  | Long-term owner/operators have resources, experience, & financial strength to manage relationship over term | 
Bid Size Flexibility | Required |  |  |  | Ability to provide 200,000 MWh/yr or 100,000 MWh/yr capacity to allow flexibility on strategy as determined by BU | 
Project Economics (strong NPV/MWh) | 30% | 3 | 1 | 2 | Financial strength based on risk-adjusted, projected cash flows, and impact on BU financial position and credit rating | The driver in a Contract for Differences is the margin modeled between the PPA price and the grid price/MWh. Favorable project economics are a prerequisite
GHG Reduction (CO2e lb/MWh) | 30% | 3 | 1 | 2 | Projected likely marginal GHG savings per MWh over the term of the project; favor projects with highest overall GHG reduction with consideration for higher early reductions | Strong correlation between high grid carbon intensity at time of renewable energy production; the purpose of is to maximize the BU’s impact on GHG reduction
Environmental& Health Co-benefits | 20% | 2 | 1 | 2 | Favor projects with lower construction and operational environmental and health impacts | 
Integration with BU on-site procurement | 10% | 1 | 1 | 1 | Integrate PPA purchases and sales into BU's energy purchasing through hedges or other mechanisms | 
Term Length | 10% | 2 | 2 | 1 | Offer 12 vs 15 year term; shorter term length ranks higher | 
Weighted Rank
Notes: Dennis

## Slide 45: Comparison of Renewable Energy Project Selection Criteria
2.5 | 1.1 | 1.8
Criteria | Weight | Solar 2 | Wind 7 | Wind 9 | Criteria Explanation | Notes
 |  | Weighted Rank |  |  |  | 
Impact New Build | Required |  |  |  | Project will generate new renewable power that would not otherwise have been generated | Project additionality is a prerequisite
Education & Research Opportunities | Required |  |  |  | Project will benefit students and faculty by allowing access to the project sites and real time data | Access to real time data and access to the project site(s) is a prerequisite
Green-e Certified RECs | Required |  |  |  | Third party certified project-based RECs | Project-based Green-e Certified RECs are necessary to validate the claims for the emissions reductions
Project Developer Financial Strength | Required |  |  |  | Long-term owner/operators have resources, experience, & financial strength to manage relationship over term | 
Bid Size Flexibility | Required |  |  |  | Ability to provide 200,000 MWh/yr or 100,000 MWh/yr capacity to allow flexibility on strategy as determined by BU | 
Project Economics (strong NPV/MWh) | 30% | 3 | 1 | 2 | Financial strength based on risk-adjusted, projected cash flows, and impact on BU financial position and credit rating | The driver in a Contract for Differences is the margin modeled between the PPA price and the grid price/MWh. Favorable project economics are a prerequisite
GHG Reduction (CO2e lb/MWh) | 30% | 3 | 1 | 2 | Projected likely marginal GHG savings per MWh over the term of the project; favor projects with highest overall GHG reduction with consideration for higher early reductions | Strong correlation between high grid carbon intensity at time of renewable energy production; the purpose of is to maximize the BU’s impact on GHG reduction
Environmental& Health Co-benefits | 20% | 2 | 1 | 2 | Favor projects with lower construction and operational environmental and health impacts | 
Integration with BU on-site procurement | 10% | 1 | 1 | 1 | Integrate PPA purchases and sales into BU's energy purchasing through hedges or other mechanisms | 
Term Length | 10% | 2 | 2 | 1 | Offer 12 vs 15 year term; shorter term length ranks higher | 
Weighted Rank
Notes: Dennis>Christen

## Slide 46: eGRID Carbon Emissions Regions Map
In most cases, eGRID Regions do not align directly with wholesale energy markets
Notes: Christen

## Slide 47: Renewable Energy Project Inventory
ERCOT
SPP
MISO
PJM
Number of Projects | 
Total | 127
Wind | 68
Solar | 59
Number of Proposals
538 unique bids
Developer Participation
36 companies
Notes: Christen

## Slide 48: Projected Economics & eGRID Impact: All
Breakeven
Relative Project Margin (Economic Benefit)
Economic Rankings represent the expected project margin (PPA Price compared to shape-adjusted power price), under natural gas driven price curve
Carbon Rankings represent the expected marginal carbon emissions reduced (in pounds of CO2 per MWh per year) that would result from each project based on the carbon intensity of the region and the project’s generation profile
eGrid Carbon Intensity (CO2e lbs/MWh)
ISO-NE
Notes: Christen
Note: ISO-NE project economics would have been below breakeven

## Slide 49: Long-list Selection Summary
Process: From the inventory of over 127 renewable energy projects, 12 were selected based on carbon intensity, economic performance, and qualitative requirements.
All of the recommended projects offer additionality, project specific Renewable Energy Credits, and a strong, credible counterparty.
Economic performance was assessed using electricity market prices derived from natural gas prices near the current Henry Hub price curve. Offers are compared by calculating the Net Present Value per Megawatt Hour of generation (NPV/MWh).
Carbon intensity was assessed by using the eGrid sub-region for each project to estimate the average CO2 lbs/MWh emissions on the grid.
Projects were ranked based on the NPV/MWh and CO2 lbs/MWh. The average of the two rankings was used for long-list selection so that economic and carbon factors were weighed equally.
Project Long-list Overview
ERCOT:
Solar: 2
Wind: 3
SPP:
Solar: 1
Wind: 6
Notes: Christen

## Slide 50: Projected Economics & eGRID Impact: Longlist
Breakeven
Relative Project Margin (Economic Benefit)
Economic Rankings represent the expected project margin (PPA Price compared to shape-adjusted power price), under natural gas driven price curve
Carbon Rankings represent the expected marginal carbon emissions reduced (in pounds of CO2 per MWh per year) that would result from each project based on the carbon intensity of the region and the project’s generation profile
eGrid Carbon Intensity (CO2e lbs/MWh)
ISO-NE
Notes: Christen
Note: ISO-NE project economics would have been below breakeven

## Slide 51: Short-list Selection Summary
Process: From the 12 longlisted projects, 5 were short-listed for final economic and emissions analysis, project due diligence and ultimate selection.
Using the Selection Criteria composed by the Energy Working Group (consisting of economic, environmental, and project / counterparty factors) the long-listed projects were ranked to determine a short-list.
Project due diligence was completed to understand the project benefits, development maturity, & counterparty strength of each offer.
All short-listed developers were notified and project offers were adjusted to reflect the most updated offer and project development status update.
Projects were ranked based on the NPV/MWh and CO2 lbs/MWh. The average of the two rankings was used for long-list selection so that economic and carbon factors were weighed equally.
Project Long-list Overview
ERCOT:
Solar: 2
Wind: 2
SPP:
Wind: 1
Notes: Casey
Dennis has talked about due diligence and christen has talked about due diligence
Ill talk about emission due diligence

## Slide 52: Annual Marginal Reduction in CO2 Emissions
Chart: lbs CO2/MWh
| Wind 7 | Wind 3 | Solar 2 | Solar 4 | Wind 9 | Wind 1 | Wind 2 | Wind 6 | Solar 3 | Wind 4 | Solar 1
 | 1404.3804 | 1294.1069 | 1211.6517 | 1211.6698 | 1284.8819 | 1408.4483 | 1403.0475 | 1401.8748 | 1364.0155 | 1283.9537 | 1211.105
Notes: Christen > Casey

## Slide 53: Final Selection Summary
Process: From the 5 shortlisted projects reviewed, 3 were identified for final economic and emissions analysis, project due diligence and ultimate selection.
Using the Selection Criteria composed by the Energy Working Group (consisting of economic, environmental, and project/counterparty factors) the long-listed projects were ranked to determine a short-list.
Project due diligence were completed to understand the project benefits, development maturity, and counterparty strength of each offer.
All short-listed developers were notified and project offers were adjusted to reflect the most updated offer and project development status update.
Final economic analysis and marginal emissions analysis are complete; informed the selection of the top projects and demonstrated energy business case for the University.
Project Long-list Overview
ERCOT:
Solar: 1
Wind: 1
SPP:
Wind: 1
Notes: Casey

## Slide 54: Alignment of Generation with Marginal Emissions: Wind 7
Chart: Generation Shape and Marginal Emissions
Wind 7 Emissions | 610.8608 | 678.4778 | 705.8301 | 731.9615 | 706.1372 | 650.9384 | 631.8284 | 665.8768 | 627.2536 | 629.634 | 607.7317 | 602.4352 | 621.1141 | 618.4103 | 617.7859 | 636.8573 | 640.8359 | 624.9624 | 619.3273 | 619.9609 | 618.3229 | 620.7412 | 579.3763 | 588.0341
Wind 7 Generation | 27.8144 | 27.3625 | 26.9054 | 26.5007 | 25.9684 | 25.4307 | 24.5652 | 21.7855 | 19.6392 | 18.7819 | 18.7077 | 19.0684 | 19.7183 | 20.1982 | 20.5503 | 20.708 | 20.766 | 21.1938 | 22.0922 | 23.7443 | 26.1106 | 27.5965 | 28.0533 | 28.0997
MW Generation
Marginal Emissions (kg/MWh)
Notes: Casey
This projects expected generation aligns well with emissions/demand trends which means it will displace dirtier generators as the marginal supplier. This has the impact of increased the amount of avoided emissions of the project.\\change legens

## Slide 55: Alignment of Generation with Marginal Emissions: Wind 9
Chart: Generation Shape and Marginal Emissions
Wind 9 Emissions | 568.3961 | 617.8914 | 675.2611 | 670.8432 | 657.1837 | 650.9617 | 581.1238 | 572.8643 | 620.589 | 609.9544 | 559.5908 | 547.6908 | 544.0973 | 531.8674 | 549.7948 | 537.8621 | 541.9276 | 542.8364 | 536.5511 | 550.7836 | 566.7292 | 548.6794 | 531.0338 | 546.4363
Wind 9 Generation | 34.3143 | 33.3152 | 31.9023 | 30.3398 | 28.6437 | 27.1359 | 25.7553 | 23.5104 | 21.6755 | 18.9323 | 17.2386 | 16.7369 | 16.1698 | 15.6603 | 15.4604 | 15.5994 | 16.0729 | 17.0559 | 20.1809 | 25.7877 | 31.8205 | 34.5813 | 35.298 | 35.0276
MW Generation
Marginal Emissions (kg/MWh)
Notes: Casey
This generation source follows emissions somewhat well but is superseded by demand/emissions at times and has peak generation during a low demand timeframe]focus on marg emissions

## Slide 56: Alignment of Generation with Marginal Emissions: Solar 2
MW Generation
Marginal Emissions (kg/MWh)
Chart: Generation Shape and Marginal Emissions
Solar 2 Emissions | 568.3961 | 617.8914 | 675.2611 | 670.8432 | 657.1837 | 650.9617 | 581.1238 | 572.8643 | 620.589 | 609.9544 | 559.5908 | 547.6908 | 544.0973 | 531.8674 | 549.7948 | 537.8621 | 541.9276 | 542.8364 | 536.5511 | 550.7836 | 566.7292 | 548.6794 | 531.0338 | 546.4363
Solar 2 Generation | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.0497 | 18.5719 | 39.5896 | 52.3311 | 59.549 | 62.3676 | 63.3173 | 63.0744 | 61.7509 | 58.1707 | 50.6153 | 34.8095 | 14.5403 | 0.61032 | 0 | 0 | 0
Notes: Casey
Generation and demand do not align. This results in the project not displacing emissions from alternative&dirtier generation sources on the grid

## Slide 57: Final Selection Summary
Project Details
  Reduce BU emissions by 53%
  15 year PPA to match 100% of BU electricity demand
  Green-e Certified project RECs Agreement
  Additionality – Agreement enabled financing for new wind farm
  Impact South Dakota (SPP) 2 to 3 times greater emissions reduction vs. ISONE
  Educational and internship opportunities for students, research for faculty
1,482 lbs. CO2e/MWh
Notes: Casey
b) 205,000 MWh/year starting in 2020 from 48.6 MW generation capacity
e) Accounting for 69,000 MTCO2e/year (of electricity emissions) > Actual impact on SPP marginal emissions 2 – 3 times more than ISO-NE

## Slide 58
Market Advantage
  45% lower PPA price than similar deal in 2015
  Contract for Differences economics work with today’s low natural gas prices
  Provides hedge on our natural gas spend
  Declining Production Tax Credit
  Thorough Market Risk Analysis
PPA Price
Market Price
Time: 15 years
Price $
Chart: Comparative NG Henry Hub Forecast Prices
Time: 15 years
Notes: c) This project provides a ~ 50% hedge on our current natural gas spend. As we complete energy efficiency projects, this will be closer to a 75% hedge at the end of the PPA period
d) We believe the declining PTC value has increased market pressure for developers to get these deals done.
e) There is a strong correlation between HH natural gas prices and electricity prices. Through a very thorough downside risk analysis we believe this project will be cash positive for us in year 1 and over the life of the project. We assume electricity prices will remain fairly flat over the next 10 to 15 years.
Went to market once in 15 and couldt afford project red line is fixed price of electricity over 15 yr period is higher than avergage market price represented by black line (variable price)
Red line has dropped by 45% so project signed will be cash positive in year 1 and over 15 years (although there will be movement over and under black line)
Hedge on nat gas not electricity purchasing
Decling PTC creates pressure in market for projects to get built which drives prices downs

## Slide 59: WattTime Third-Party Validation
About WattTime
Environmental nonprofit founded by UC Berkeley researchers
Powered by > 200 expert volunteers from Berkeley, Google, Microsoft, US DOE, PG&E, etc
Spun into the Rocky Mountain Institute in 2017
As renewable energy grows, increasing difference between the emissions consequences of using energy at a particular time and place
Our mission is to research, raise awareness of, and spread common practical tools for optimizing when, where, and whether to use electricity
Our role in this project
Met BU through Boston Green Ribbon Commission collaboration
Neutral third-party nonprofit technical review of the analysis
Notes: Gavin

## Slide 60: The “marginal” generator

## Slide 61: Two ways to measure
Old way: use theory to estimate
New way: use data to measure
Notes: Gavin

## Slide 62: Emissions factors vary over time…

## Slide 63: …and space

## Slide 64: Greenhouse Gas Protocol
Scope 2 carbon: inventory
All MWh are treated equally
Does not consider variation over time
RE assumed to displace all power plants equally
Accounting abstraction
Applies to all RE regardless of quality
Advantages
  Simple
  Ensures all emissions are “owned” by someone
GHGP says institutions must report
Avoided emissions: impact
Each MWh’s impact is measured
Considers variation over time
Considers which power plants are actually displaced (“marginal” emissions)
Scientific measurement
Only applies to projects with additionality
Advantages
  Measures true emissions impacts
  Makes optimization possible
GHGP says institutions may report

## Slide 65: Calculation Methodology
BU
Narrowed project list to short list
Provided geographic locations
CMU
Provided marginal emissions rates by time and region from 2006-2016
Edison
Provided 8760 generation estimates by time and site
Multiplied generation (in MWh), by marginal emissions data (in lbs/MWh) for each time to generate emissions saved in each period and site
Added up and divided by project size to generate common metric of lbs/MWh by site
WattTime
Examined BU’s short list
Generated own marginal emissions factors using a different methodology
  Different underlying statistical algorithm
  Based on real-time, 5-minute rather than historical, hourly
  Based on Blancing Authority rather than NERC region
Examined Edison’s 8760 data
Reproduced all calculations and compared
Notes: Gavin

## Slide 66: Results
Notes: Gavin

## Slide 67: WattTime Validation Conclusion
The approach used to calculate the avoided emissions of the projects under consideration is fundamentally sound.
  Use the latest solid, peer-reviewed science
  Generated from empirically derived techniques validated against real data, not theoretical models
  Accurately reflect the operation of the grid in the defined regions
  Calculations accurately implemented
  Contract clause to remeasure each year
BU’s unique choice accurately identified the best locations and BU’s choices caused significant, real-world emissions reductions.
In fact, WattTime concluded that BU likely understated the true emissions benefits of their choice
This is because more granular analysis found that the particular location within SPP caused ever larger avoided emissions than an average location within SPP
Notes: Gavin

## Slide 68: Not All MWh Are Created Equal
Electricity
Natural Gas
Steam
Oil
Efficiency
Impact beyond
1 REC = 1 MWh
If BU had bought locally, each MWh = 803 lbs CO2
At the sites BU picked, each MWh = 1,692 lbs CO2
This strategy more than doubled real-world emissions impacts
Making BU net negative: if BU ceased to exist, global emissions would increase
Grid
Renewables
Electrification with Renewables
Offsets
Notes: Gavin

## Slide 69: What if all RE purchases optimized for emissions?
WattTime estimated what would happen if everyone adopted this strategy
Obtained new renewable energy build globally, each year, by country (from EIA)
Matched with approximate marginal emissions rates at those locations
Compared with emissions at highest-impact locations
Results were 4.3 gigatons of savings per year
That’s approximately the same impact as converting the entire United States to 100% renewable energy

## Slide 70: Thank You
Boston University
  Dennis Carlberg, Associate VP for University Sustainability carlberg@bu.edu
  Casey Kelly, sustainability@BU Intern caseyk@bu.edu
Carnegie Mellon University, Center for Climate and Energy Decision Making
  Inês Azevedo, Co-Director iazevedo@cmu.edu
Edison Energy (formerly Altenex)
  Christen Blum, christen.blum@edisonenergy.com Advisory Renewables Managing Director
WattTime
  Gavin McCormack, Co-Founder and Executive Director gavin@watttime.org

## Slide 71: Appendix: Opportunities for further research
More geographic granularity
  Northern SPP vs southern SPP
Align with grid dispatch (balancing authority regions)
Consider renewable energy curtailment
Notes: Gavin

## Slide 72: Appendix: the problem with increasing granularity without using the right data
2,115 lbs CO2/MWh
0 lbs CO2/MWh

## Slide 73: Appendix: what universities do will heavily influence rising corporate RE tide

## Slide 74: Appendix: BRC members are doing this to support a diverse set of sustainability goals
Price/total spend/volatility of spend
Meeting sustainability goals
The value of the hedge
Additionality / marketing claims
Minimizing downside risk vs. maximizing NPV or upside
Wider social good from renewables development
Clear exit options and costs
Avoiding/triggering mark to market accounting, or capitalization
Locating generation close to load
Carbon impact
BUYER PRIORITIES