## Slide 1
James Pigeon
MANAGER, DISTRIBUTED RESOURCES INTEGRATION
NPCC Regional Standards Committee October 15, 2020, Virtual Conference
NYISO DER Participation Model:
Aggregations & Roadmap

## Slide 2: FERC Order No. 2222
FERC issued Order No. 2222 (Participation of Distributed Energy Resource Aggregations in Markets Operated by RTOs and ISOs) on September 17, 2020.
The description of the NYISO’s DER market design reflects the rules accepted by FERC in December 2019.
The NYISO is still evaluating whether and what changes to its rules may be necessary to comply with Order No. 2222, and therefore the concepts and rules described in this presentation may change.

## Slide 3: DER Definition for the Market Design
Distributed Energy Resource (“DER”): (i) a facility comprising two or more Resource types behind a single point of interconnection with an Injection Limit of 20 MW or less; or (ii) a Demand Side Resource; or (iii) a Generator with an Injection Limit of 20 MW or less, that is electrically located in the NYCA.
DER must be capable of responding in real-time to NYISO dispatch instructions.

## Slide 4
Transmission Nodes

## Slide 5: Transmission Node Overview
The ISO, in coordination with the Transmission Owners, shall establish the set of Transmission Nodes in the New York Control Area
  All Transmission Nodes will be identified in ISO Procedures
Aggregators will work with Transmission Owners to determine which ISO identified Transmission Node each individual DER/Facility electrically maps to
  Only DER/Facilities that map to the same Transmission Node may be aggregated together
Aggregators may enroll one or more Aggregations at a Transmission Node

## Slide 6: Transmission Node Background
Transmission Nodes reflect the collection of electrically similar facilities to which individual DER may aggregate as an Aggregation with a single PTID
The DER Roadmap outlined the need to:
  Consider all Transmission Nodes that allow the NYISO to best represent DERs impact on the transmission system
  Deliver more granular pricing data to incent efficient locational investment

## Slide 7
DER Aggregations: Overview, Rules & Participation

## Slide 8: DER Aggregation Approach
Aggregations grouped at a Transmission node allow the NYISO to continue to support system reliability leveraging its wholesale markets
  Requiring Aggregations at Transmission Nodes will allow the NYISO to effectuate dispatch in a manner that will effectively secure transmission constraints on the system while sending efficient price signals
  This Transmission Node level granularity, instead of Load Zone level, will more effectively relieve transmission constraints thereby resulting in lower overall total production cost

## Slide 9: DER Market Participation
The DER participation model will only be available to Aggregations
  An Aggregation consists of two or more individual resources, except that Demand Side Resources and individual facilities that can reduce load and inject energy (i.e., transition from being Load to Supply without an infeasible operating range), will be permitted to individually use the DER participation model as a single-resource Aggregation
Individual facilities in an Aggregation will participate under the market rules for either:
  A DER Aggregation (when there are multiple Resource types in the Aggregation), or
  The specific Resource type (when there is a single Resource type in the Aggregation)
    For an Aggregation of Intermittent Power Resources, the technology type of each Resource in the Aggregation must be the same (E.g., Resources depending on wind as their fuel)

## Slide 10: Basics for all Types of Aggregations
Resources will be permitted to aggregate to meet minimum requirements and performance obligations for eligible participation models
The Aggregator will be the NYISO Market Participant
The Aggregation will be a group of one or more resources participating in the NYISO Market, represented by a PTID
  Bids will represent the offer of the Aggregation
  Performance will be measured in aggregate
  Financial settlements will be in aggregate
    The NYISO intends to separately process the injection, withdrawal and load reduction data to ensure accurate settlements

## Slide 11: Aggregation & Ancillary Services
Aggregations will be eligible to supply the Ancillary Service Products for which all DER within the Aggregation are eligible to supply
  Example 1: An Aggregation would be eligible to supply Regulation only if all DER in the Aggregation are eligible to supply Regulation
  Example 2: If one resource in the Aggregation is only eligible to supply 30-Minute Non-Synchronous Reserves, the entire Aggregation is only eligible to supply 30-Minute Non-Synchronous Reserves

## Slide 12
Dual Participation

## Slide 13: Dual Participation
The NYISO’s market design allows resources that provide Wholesale Market services to also provide services to another entity (e.g., the utility or a host facility)
  The NYISO believes that providing resources with the flexibility to meet wholesale and distribution system needs will deliver the maximum benefit to New York electricity consumers
  Resources participating in the wholesale markets will continue to be obligated to follow all applicable NYISO market rules and utilize good utility practices
Dual participation concept applies to all resources, not just DER Aggregations
  Effective May 1, 2020, Generators and Demand Side Resources electrically located in the NYCA may simultaneously participate in the ISO-administered wholesale markets and in programs or markets operated to meet the needs of distribution systems located in the NYCA.

## Slide 14: Requirements
Dual participating resources are required to:
  Comply with all NYISO market rules for the services offered to the wholesale market
    Non-compliance may result in financial penalties
  Appropriately offer into the wholesale markets to reflect any non-wholesale (e.g., retail) obligations
    Resources are required to follow NYISO dispatch instructions at all times;
    Resources submit offers to NYISO when providing non-wholesale service
    Resources receive payments for Energy or Ancillary Services scheduled through these offers

## Slide 15: Next Steps
Q2 2021: Deploy SD-WAN infrastructure for additional secure communications of scada data
Q4 2022: Deploy software to enable participation of DER aggregations

## Slide 16: Our mission, in collaboration with our stakeholders, is to serve the public interest and provide benefit to consumers by:
  Maintaining and enhancing regional reliability
  Operating open, fair and competitive wholesale electricity markets
  Planning the power system for the future
  Providing factual information to policymakers, stakeholders and investors in the power system