## Slide 1
Thinh Nguyen
Senior Manager, Interconnection Projects
NPCC Regional Standards Committee
October 15, 2020
DER Interconnection Requirements

## Slide 2: Agenda
Background
Interconnection Process for DERs

## Slide 3
Background

## Slide 4: Background*
Today’s presentation will review NYISO’s interconnection process for DERs seeking the following interconnection services:
  Energy Resource Interconnection Service (ERIS)
  Capacity Resource Interconnection Service (CRIS)
*FERC issued Order No. 2222 (Participation of Distributed Energy Resource Aggregations in Markets Operated by RTOs and ISOs) on September 17, 2020. The NYISO is currently evaluating what changes to the rules and processes discussed in this presentation, if any, may be necessary to comply with Order No. 2222.

## Slide 5
Interconnection Process for DERs

## Slide 6: Interconnection Processes Applicable to DERs
NYISO’s interconnection procedures govern the interconnection of the facility if:
  Developer intends to make wholesale sales and
  Developer proposes to interconnect to (i) transmission or (ii) distribution facilities on which there is already a generator making wholesale sales (i.e., “FERC-jurisdictional distribution”)
NY Standardized Interconnection Requirements (SIR) govern the interconnection of the facility if:
  Developer is interconnecting to portions of the distribution system other than “FERC-jurisdictional distribution” and the resource is less than or equal to 5 MW
Utility interconnection procedures govern the interconnection of resources if the interconnection is not subject to the NYISO or SIR processes
  Interconnection Service for SIR or Utility-level interconnection is based on the applicable interconnection agreement
  Facilities that proceed through the SIR or utility interconnection processes must have an interconnection agreement that allows wholesale sales

## Slide 7: Determining the Applicable Interconnection Process for ERIS
A developer may request a determination from the NYISO regarding whether its proposed interconnection is subject to the NYISO’s SGIP
  This may be requested under Section 32.1.1.4 of Attachment Z to the OATT
  This may also be requested as part of a pre-application request (a $1000 request for information regarding a proposed interconnection prior to submitting an Interconnection Request)
    See Section 32.1.2 of Attachment Z to the OATT

## Slide 8: Determining the Applicable Interconnection Process for ERIS (cont.)

## Slide 9: Determining the Applicable Interconnection Process for ERIS (cont.)

## Slide 10: NYISO’s SGIP
NYISO SGIP (OATT Attachment Z) is the NYISO’s interconnection process for the following Small Generating Facilities 20 MW or less:
  New facilities 20 MW or less that meet both of the following criteria:
    Facility proposes to interconnect to FERC-jurisdictional facilities (i.e., transmission facilities or distribution facilities on which there is already a generator making wholesale sales); and
    Facility intends to make wholesale sales (via injection)
  Existing facilities 20 MW or less that make material modifications or material increases to their facilities
    If an increase to the facility results in the facility exceeding 20 MW, the modification/increase is subject to the Large Facility Interconnection Procedure
    Qualifying Facilities that seek the right to participate in the wholesale market will be studied in the NYISO’s interconnection process under certain circumstances (depending upon the proposed point of interconnection, whether the facility is new, whether, if existing, the facility increasing its output, etc.)

## Slide 11: NYISO’s Interconnection Queue Administration
Projects assigned Queue position based on date Interconnection Request (IR) received
  Demonstration of Site Control is required with a Small Generator IR
NYISO Queue is not a “Hard Queue” in which IRs are evaluated in sequential order
  Projects can advance on different schedules
  Small generators may be studied in clusters if interconnecting in close proximity (See Att. Z, Section 32.3.5.3.2)
Status of Queue Projects is updated monthly on NYISO public website

## Slide 12: SGIP – Normal Study Process
Optional Feasibility Study (FES)
  Customer may opt to waive the FES unless it proposes multiple POIs
  FES is a high level study that evaluates proposed Point of Interconnection (and alternative POIs as requested) and the proposed configuration
  The focus of the FES is on the local system
  FES study report includes preliminary nonbinding cost estimate for SUFs
System Impact Study (SIS)
  May be waived upon mutual agreement of customer, NYISO and CTO
  Intermediate level study that evaluates project impact on system reliability
  Includes updated nonbinding cost estimate for SUFs
  Not subject to review by stakeholders and does not require Operating Committee approval
Facilities Study (FS)
  May be waived upon mutual agreement of customer, NYISO and CTO
  Facilities Study determines binding cost estimates and cost allocation for Local SUFs
  Not subject to a Class Year study unless non-Local SUFs are identified (or the project is larger than 2 MW and requesting CRIS)

## Slide 13: Process for Evaluation of CRIS Requests
Resources larger than 2 MW requesting CRIS
  Required for any resource larger than 2 MW that requests CRIS – even if the resource is not subject to the NYISO’s interconnection procedures
  CRIS request must be evaluated in a Class Year Study or Expedited Deliverability Study
    Class Year Study evaluates a group of CRIS requests together and determines deliverability and if not deliverable, the respective cost allocation for System Deliverability Upgrades
    Expedited Deliverability Study evaluates a group of CRIS requests together and determines whether the requested CRIS are deliverable or not
      No cost allocation

## Slide 14: Our mission, in collaboration with our stakeholders, is to serve the public interest and provide benefit to consumers by:
  Maintaining and enhancing regional reliability
  Operating open, fair and competitive wholesale electricity markets
  Planning the power system for the future
  Providing factual information to policymakers, stakeholders and investors in the power system