## Slide 1: Wireless The Headache You Can’t See… Part Deux!
Vikas Khanna
V.P. Broadband Technologies
Covad Communications
vikas[at]covad.com

## Slide 2: Agenda
Why Fixed-Wireless ?
Technology
  Pre-WiMax (non-standardized)
  WiMax (802.16d)
New Challenges & Lessons with WiMax
What’s next?
  Network Everywhere… WiMax / LTE  FMC

## Slide 3: Why Fixed Wireless?

## Slide 4: Why Fixed-Wireless?
Business is still booming…
  The fixed/portable broadband wireless access equipment market (sub-11 GHz) has grown from US$562 million in 2005 to US$1.2 billion in 2007.
  At the end of 2007, there were 1.6M BWA (Broadband Wireless Access) and WiMax subscribers.
  Asia/Pacific presents major growth sectors due to limited facilities infrastructure in certain countries.
  Primary service delivery method is Ethernet… which is projected to be a $40B market in 5 years.

## Slide 5: Why Fixed Wireless?
Broadband Stimulus Update American Recovery & Reinvestment Act, 2009
Broadband Program - $7.2B
  Rural Utilities Service (RUS) - $2.5B
    Existing RUS Loans Program has $690M for FY 2009
    Additional $2.5B Funding
  National Telecommunications & Information Administration (NTIA) - $4.7B
Purposes of program: provide broadband access to consumers residing in unserved areas .
Provide improved broadband access to consumers residing in underserved areas .
March 27th, 2009: Proxim Wireless Corporation announced that a new community in Missouri has been built using Proxim's wireless technology to provide the entire town the capability of broadband access, wireless VoIP, and video surveillance. $4K savings per month over land-line facilities.
May 27th, 2009: Iberbanda, Spain’s leading WiMax carrier selects Alvarion to expand 3.5GHz WiMax network in Catalonia (covering an area of over 32,000 square kilometers, is divided into four provinces: Barcelona, Tarragona, Lleida and Girona)

## Slide 6: Technology

## Slide 7: Technology
Fixed Wireless – Last Mile
  Microwave Technology (RF) – WiMAX / Pre-WiMAX
  Not WiFi (802.11x) or Cellular (GPRS, UMTS, HSPDA)
Backbone Network Equipment
  Technology: TDM (older), Ethernet (newer), Combined (MEF Certified)
  Frequencies: 6GHz to 38GHz licensed frequencies
  Point-to-Point Deployment (some radio vendors support mesh architecture)
  Range: up to 10 miles between sites (depending on frequency and capacity requirements)
  QoS, Ultra-low latency (industry standards drive improvements)
  High Capacity
    up to 500Mbps (per channel) – dual pole up to 1 Gbps (<38 GHz )
    High-Cap (1 Gbps/ channel) possible at higher frequencies but with limited range

## Slide 8: Technology: Access Network
Pre-WiMax:
  No IEEE Standard (no interoperability)
  Frequencies: 2.4GHz / 5GHz unlicensed spectrum
  Coverage: typically up to 8 miles (additional distance possible with external antenna)
  Capacity: Limited, up to 10Mbps (over 15 MHz channel)
  LOS (Line of Sight) to AP – typically required
  Products reaching end-of-life!
WiMax:
  IEEE Standard: 802.16-2004 (aka 802.16d) – supports interoperability!
  Frequencies: 3.65GHz, and 5.x GHz unlicensed spectrum
  Coverage: up to 8 miles but provides wider coverage due to NLoS support
  Capacity: up to 45Mbps* (over 15 MHz channel )
  NLoS (Non Line of Sight) Support: Subscriber units are available for both indoor / outdoor
    Indoor units suffer from greater signal loss due to environment thereby limiting overall performance in comparison to externally mounted unit.
  Improved spectral efficiency
  Support for VLANs, QoS/ CoS, Protocols (ex: OSPF/BGP ), improved processors…

## Slide 9: Technology: Equipment
Access Point
Subscriber Unit (CPE)
Backhaul
It still looks the same!

## Slide 10: Challenges & Lessons Learned (Some old… some new)

## Slide 11: Challenges: Deployment
Must haves!!
LOS (Line of Sight) Not really… depends on gear.
Available Frequency YES!!! (No Change)
Cabling / Internal Wiring YES!!! (No Change)
Roof Access (space on roof?) YES!!! (No Change)
Weather Proofing YES!!! (No Change)
Power YES!!! (No Change)
Tools (ex: Crane, Helicopter) YES!!! (No Change)
FCC/FAA Permission YES!!! (No Change)
City/State Permits YES!!! (No Change)
While the technology and features have greatly improved, the physical properties for most equipment remains the same…

## Slide 12: Challenges: Deployment (cont’d)
18 GHz
18 GHz
11 GHz
23 GHz
Cellular
WiMax
Access
Point
Equipment installations have become easier due to advances in mounting apparatus – but, you still have to deal with legacy infrastructure… (interop w/ existing mounts, etc)

## Slide 13: Challenges: RF Spectrum Management
Licensed Spectrum (Back Haul):
  Requires FCC prior-coordination to ‘light up’ microwave between two points (application approval can take up to 90 days)
  FCC ‘rules’ govern your network build out
    Illegal to turn up link without frequency PCN – can get fined!
    If requested frequency isn’t available, you can’t use your “engineered” design
  Requires true engineering (path profiling, link budget, site surveys, power limitations, weather, etc)
    In-house work can turnaround within a couple of business days – if you require a site visit or structural analysis you could be waiting days, weeks, even months!
  FCC does not guarantee interference free communication on a licensed path
    There are violators out there!
No Change in Process

## Slide 14: Challenges: RF Spectrum Management
Unlicensed Spectrum (Access Network):
  UNII band (part 15) – first come, first serve spectrum use so you have to find a way to co-exist with other WISP’s or operators using the same unlicensed band
    Illegal to restrict other operators just because you were there first!
    Landlords are aware of this rule and therefore you can’t have exclusivity in your contracts when it comes to spectrum usage
  Ever changing environment – today your link works and tomorrow it doesn’t because someone turned up new gear in the same frequency (or in your path).
  New band (5.47-5.725 GHz) offers new opportunities.
    Requirement to coexist with Radar – DFS (Dynamic Frequency Selection) implementation a MUST!

## Slide 15: Challenges: RF Spectrum Management
It’s still a jungle out there… but now, you have to find a way to co-exist between old and new technology! “First come, First serve” – new equipment may have broader array of change options available whereas legacy equipment does not!

## Slide 16: Challenges: Provisioning and Management
Pre-WiMax:
  Provided for direct CLI-access into CPE for provisioning
  Remote: direct telnet into equipment by NOC for assistance
  Manual, not much user friendly provisioning, management and troubleshooting
  Time consuming installs with many steps through CLI and offers limited stats for troubleshooting
WiMax:
  New systems offer web-based provisioning or EMS configuration via over-the-air download.
  More steps required for initial setup in the provisioning server
  Requires expertise and knowledge of WiMAX standard to set up services/ templates
  Remote: no telnet access – manage via Web or single EMS.
  Field technicians need some time to adapt to the new tools and technology

## Slide 17: Lessons Learned: RF Management
Multiple channel sizes in WiMAX offer options in congested RF environments and better spectrum management
  Select channel size depending upon RF spectrum available
  Higher spectral efficiency means higher or at least similar bandwidths as on legacy pre-WiMAX hardware
Improved link budgets and adaptive modulation mean more resilience to interference / noise
OFDM offers resilience to multipath and improved availability
Requires Intelligent Radar Detection Algorithms to operate in new DFS band
  Equipment prone to radar detection upon which either shut down or change channel
  Requires one or more backup channels
GPS synchronization across network lowers intra-network self induced interference

## Slide 18: Lessons Learned: Provisioning
WiMAX APs and CPEs are designed for rapid outdoor installation with remote automated provisioning and configuration through EMS.
Template based provisioning allows fast commissioning
Automatic discovery of network elements
Provisioning Servers auto-provision CPEs in database
Bulk Upgrade
  Streamlines updates to AP and PE device firmware.
Different User Group Categories to minimize security Risks
  Different access rights of authorized users

## Slide 19: What’s Next?

## Slide 20: WiMAX Applications
Traditional Fixed Broadband Wireless Access
  Offers all services and features expected by BWA customers
  Typically installed in hours, days --- not weeks, months!
“Personal Broadband”
  Service can be delivered directly to a person’s device, not a location
Backhaul (e.g. rural locations)
  Traffic up to 50 Mbps
Voice/Video over WiMAX
  Enhanced QoS and packet classification ensure high quality service

## Slide 21: What’s next?
FMC: Fixed-Mobile Convergence
  Implementations of call/ session continuity - seamless mobility between VoWiFi and cellular/mobile WiMAX networks
  Devices that support cellular/mobile WiMAX & WiFi (Samsung SWD-M100 Mondi)
  Fixed WiMAX CPEs with integrated WiFi Access Point
    Fixed WiMAX connection backhauls the data once connection is on WiFi network
Is it LTE? (Long Term Evolution)
  Depends on who you are! (2/18/09: Verizon chooses LTE Vendors)
  Long Term Evolution: “4G” (Mass adoption by 2012?)
    Incumbent mobile cellular operators favor LTE as a natural extension to their networks
Is it WiMax? (Network World: WiMax changes lives in rural Thailand)
    Its available now and being deployed – first to market advantage
    Potential ‘forklift’ upgrade – ideal for Greenfield deployments but may not be cost-effective for existing network upgrade

## Slide 22: END
Q&A
Vikas Khanna
V.P. Broadband Technologies
Covad Communications
vikas[at]covad.com
Ranjiv Saini
Mgr., RF Technologies
Covad Wireless
rsaini[at]covad.com
(not in attendance but you can contact for questions)