## Slide 1: Integrating Renewables into the Grid
James Loewen
Goshen College Science Speaker Series
January 16, 2019

## Slide 2: This talk
Electricity and sustainability: potential employers and careers
Integrating renewables into the grid. What? Why? How?

## Slide 3: Energy and sustainability
Appliance Efficiency Standards
Wind Farm Siting Rules
Trade Tariffs (Solar Panels)
Rooftop Solar Rebates
Forest Management
Transit
Subsidies
Transmission Lines
Ethanol
Subsidies
Environmental Impact Studies
Electric Utility Rates
Integrating Solar and Wind into the Grid
CAFÉ Standards
Weather Stripping
Carbon Capture and Storage (CCS)
Electric Cars
Cap ‘n’ Trade
Elections in South America
Fracking Restrictions

## Slide 4: Grids and Renewables: the Players
Federal government: Energy Info Administration (data), EPA (environment), DOE (nuclear power), Dept. of Commerce (trade tariffs), Dept. of State and Dept. of Defense (foreign wars and peace), FERC, Federal labs (NREL, LBNL, LLNL, White Sands, Sandia, Oak Ridge, etc.)
State governments: public utilities commissions, state EPAs, depts. of transportation, etc.
Cities and counties: offices of sustainability, solar rebates, transit electrification, etc.
Utilities: privately owned, publicly owned
Para-governmental organizations (RTOs, ISOs, WECCs)
Manufacturers: cars, buses, wind turbines, solar panels, appliances, windows, HVAC, batteries, etc.
Finance: banks, institutional investors, local governments (PACE), etc.
Installers and builders: solar, wind, fossil gen, nukes, transmission lines, distribution lines, etc.
Non-profits: Sierra Club, Green Peace, The Nature Conservancy, consumer advocates, etc.
Universities and colleges
International: World Bank, UNEP, IEA
Consultants

## Slide 5: What professions are involved?
Hard sciences: physics, chemistry, biology
Environmental science, policy, and management
Engineering
Economics
Business
Communications
Law
Policy
Teaching
Preaching
Politics: federal, state, local
Etc.

## Slide 6: Integrating renewables into the grid
What?
Why?
How?

## Slide 7: Utility infrastructure
Utility-Scale Storage
Distributed Storage
Plug-in Electric Vehicles
Rooftop Solar

## Slide 8: Special characteristics of electricity
Need (near) total reliability
Supply must meet demand from second to second
Storing electricity is difficult and expensive
Dangerous commodity
Grids are natural monopolies (economies of scale)

## Slide 9: Policy Goals for the Grid
Safety
Reliability
Affordability
Low environmental impact
  Global/greenhouse gasses (GHGs): CO2 and methane
  Local/environmental justice: SOx, NOx, particulate matter
  Thermal pollution of rivers and oceans
  Water consumption (once-through cooling for thermal plants)

## Slide 10: GHGs: the Grid vs. the Rest
California CEC June 2018. Deep Decarbonization in a High Renewables Future

## Slide 11: How to pollute less?
[Fewer people]
Reduce electric use: fewer kWh per customer; fewer kWh per dollar of output
Make the grid cleaner (power from less polluting sources)

## Slide 12: Usage per capita

## Slide 13: Lower use per customer. How?
Energy Efficiency programs:
  Houses and commercial buildings:
    Passive measures (the shell)
    Active measures (lighting and HVAC)
  Appliances: California’s Title 24
Rate design, high marginal rates (can lead to other challenges)
Mild climate

## Slide 14: How to make the grid cleaner?
Traditional non-GHG energy sources: big hydro and nuclear
  Pros
  Cons
“New” clean sources:
  Wind, solar, geothermal (e.g. geysers), biofuel, wave, tidal
  (Transmission)
NIMBY

## Slide 15: How much do new renewables cost?
Lazard, November 2018

## Slide 16: Cost Trends

## Slide 17: Solar Cost Components
NREL September 2017

## Slide 18: Renewables are Exploding

## Slide 19: Renewables are already cheap! So, what’s the problem?
Resource costs vary by geography
Intermittent and non-dispatchable

## Slide 20: Sunny spots

## Slide 21: Where the wind blows

## Slide 22: December 19, 2018 net demand in CA

## Slide 23: Total CA “load” minus renewable generation: The Duck Curve

## Slide 24: Duck hunting
Lots of gen sources – the “law of large numbers” – spread over large area
Lots of wires: transmission and distribution
A “diversified portfolio”, e.g., wind plus solar plus biomass plus…
Energy storage
Customer incentives: time of use (TOU) rates, demand charges
Overbuilding/curtailment of renewables
Keep some fossil for the last 10% – 20%
Virtual: Purchases RECs (renewable energy credits)

## Slide 25: Ways to store energy
Mechanical inertia: flywheel
Pumped hydro
Other mechanical gravity: rails, conveyor belts, cylinders, etc.
Chemical: Hydrogen; converted biomass
Thermal: molten salt (from solar)
Electro-chemical batteries

## Slide 26: Key battery characteristics:
Installed cost per kW
Installed cost per kWh (or, how many hours at the peak kW)?
How fast to charge? (especially for cars)
Round trip efficiency
Durability (rate of degradation per cycle)
Compactness and weight. Important for
  Cars/trucks/buses
  Customer-sited vs. residential grid vs. wilderness grid
Environmental impact (is it toxic?)
Supply security (is the metal/mineral mined in Russia, China, Congo?)

## Slide 27: Cost trends for batteries

## Slide 28: Is wind a better bet?

## Slide 29: Wind (cont’d)
Texas example:
  “Scientists found that between wind energy from West Texas and the Gulf Coast, and solar energy across the state, Texas could meet a significant portion of its electricity demand from renewable power without extensive battery storage. The reason: These sources generate power at different times of day, meaning that coordinating them could replace production from coal-fired plants.” [Houston Chronicle, re Rice University study]
Off-shore wind:
  More constant (less intermittent)
  Less NIMBYism
  More expensive, but costs are dropping

## Slide 30: The cheapest solution…
Really depends on:
Local “load” (consumption profile),
Natural resources available (e.g. Norway, Nevada, Wyoming)
Historical infrastructure (France)
Cost trends for batteries
Etc.

## Slide 31: In CA, up to 90% renewable is easy…
"Simulations show up to 90% of California's power can come from a combination of wind, solar, batteries and geothermal," E3 Senior Partner Arne Olsen told Utility Dive. "Beyond 90%, it gets difficult and expensive.“ [Utility Dive]

## Slide 32: What about electric cars?
Environmental impact – how clean is the grid
Electric grid needs to expand
Batteries help grid as mobile storage - but they also wear out the batteries.
Utilities love EVs
Takeaway: positive but complicated

## Slide 33: Rooftop solar is great, right?
Well, not so fast
  From Lazard, utility scale solar farms are MUCH cheaper
  “Net energy metering” is a subsidy
So how come everyone likes rooftop solar?
  Costs are hidden
  Benefits are visible and financially tangible to the gen owner
  It’s really making solar energy
  Employs a lot of installers
I would do it if I had the chance

## Slide 34: NIPSCO plans to go green
Coal contribution to NIPSCO mix
  2018 – 65 %
  2023 – 15 %
  2028 – 0 %
Will replace with:
  1,500 MW of solar with battery backup
  150 MW of wind
  125 MW of reduced demand through efficiency and demand-side management programs
  50 MW of electricity purchased from other utilities, all by 2028.
Claims long run savings of $4 billion. Requests 12% rate hike now.

## Slide 35
Thank you!
james@everspring-energy.com

## Slide 36
Backup Slides

## Slide 37: Seasonal mismatch – demand vs. renewables

## Slide 38: Battery manufacturers

## Slide 39: Cost of Lithium Ion Battery Inputs

## Slide 40: Grid modernization
Investments in distribution and transmission system technologies that improve the grid's reliability, resilience and efficiency. They range from advanced metering infrastructure (AMI) to distributed energy resources (DER) to smart grid and automation hardware and software.
Very much in favor
Very expensive

## Slide 41: The Western Grid - 2020

## Slide 42: Storage for peak shaving

## Slide 43: Different battery technologies
Lithium batteries: many different sub-chemistries
Flow batteries: industrial scale, cheaper, slower to charge, less efficient, more durable, not appropriate for customer-sited
Many press releases from labs, but getting to commercial volume is a whole different challenge

## Slide 44: Gas peakers instead of storage

## Slide 45: How storage can help the grid